## Slide 1: Hazardous* Materials Handling
Viraj, Katie, & Marisa

## Slide 2: Before
Protective gear when using hazardous equipment (i.e. closed-toed shoes, gloves, goggles)
Signage for warning (descriptive: biological hazards or fire hazards) on locations of assistance (eyewash stations, safety showers, extinguishers) and chemicals and waste receptacles
Proper trainings to ensure proper understanding of materials and possible dangers (experiment specific).
  Identifying job-specifics hazards (i.e. machinery) & safety procedures
  Designate a Chemical Safety Officer
Handling Glassware
  Check condition of glass
  Proper hand protection when picking up broken glass

## Slide 3: Handling & Transportation of Chemicals
Assume all chemicals are potentially hazardous
Never attempt to pick up a bottle by the cap
Large bottles carried on a wheeled cart; be cautious of obstructions
  Incompatible chemicals should not be carried on the same cart
Proper labeling
Hazardous chemicals should always be attended to
Unstable materials should not be moved
Special flammable storage areas for organic solvents
  Special rubber carriers

## Slide 4: Emergency Situation
-Includes Cuts, Burns, Chemical Spills, Mercury Poisoning, Explosions, Chemical Inhalation, etc.
-How one reacts is likely based on what chemical is involved and the the extent of the injury.
-The emergency shower/eyewash station in the back corner of the room is relevant to these situations.

## Slide 5: Chemical Storage
Always return a chemical to its storage location
Be aware of chemical compatibility
  Solvents, acids, bases, reactives, oxidizers and toxins should be stored separately
Hazardous chemicals* should not be storage on the floor
Do not move unstable, explosive, or unusually hazardous materials due to size or toxicity
Minimize transport when available
  Identify & document storage locations
Containers must be:
  Free of rust & deformation
  Compatible with chemical
When working at an individual workstation, you should only hold a small quantity.

## Slide 6: Chemical Disposal
Waste container should be capped, labeled, & compatible with waste
  Label is called “packing manifest”; a manifest must be attached to each cardboard box for each hazard class and include lab information and waste information
Waste minimization
Flammable organic solvents: many can be reused for fuel unless extremely toxic
Do not mix wastes
Smallest container possible
Do not pour down the sink
Record disposal
Substitute: whenever possible, substitute nonhazardous, biodegradable chemicals for hazardous chemicals in order to reduce volume of hazardous waste